## Slide 1: Iwiggle: robot follower
Andrey Pak - Donatas Kozlovskis
Enric Cornellà - Fernando Garcia - Igor Péric
12/12/2014
Notes: Ferran

## Slide 2: Outline
  Introduction
    Objectives
    Motivation
  Game Description
  Project management
  Hardware overview
  System design
      State machine
      Vision module
      Motion module
      I/O module
  Limitations and issues
  Conclusions
  Further improvements
12/12/2014
2
Notes: Ferran

## Slide 3: Objectives I
Interactive game
Introduce robotics to children
Friendly manner
Enhancing learning
Constraints
Sign detection based
Accuracy in detection
Robust
Strong feedback
12/12/2014
3
Notes: Ferran
The main goal of the Project is to design a robot platform to introduce robotics to children

## Slide 4: Objectives II
  Read colored markers on the floor
  Sign classification
  Implement action responses
  Review the hardware design
  Implement controller for sensors and actuators
  Real-time solution
Notes: Ferran
Read marker, classify and define action response
The hardware design may be review in order to satisfy all requirements
Implement controller for all sensors and actuators
All requirements

## Slide 5: Motivation
Why is this topic worth it…?
“Dynamic and friendly experiences such as interactive games enhance
the learning experience of children at schools”
12/12/2014
4
How people learn: Brain, mind, experience, and school. Bransford, John D. (Ed); Brown
Notes: Ferran

## Slide 6: Game description
12/12/2014
5
?
Notes: Ferran
But what is about?

## Slide 7: Project Management
Division
Gantt diagram
Notes: Ferran

## Slide 8: Hardware overview
Vision Module
Motion Module
I/O Module
State Manager
Notes: Ferran
The whole system is managed by the state machine
Then we have tree different parts: visión, motion and I/O

## Slide 9: Vision Module
  Flowchart
Color Image
Segmented Image
Object Shape
Sign classification
Angle detection
Notes: Donatas
handle the image data acquired from Raspbery Pi camera. This
handling includes two basic subtasks: sign detection and sign recognition (classication).

## Slide 10: VM – inverse perspective transform
Input
Output
Notes: Donatas
Simple homography matrix
Small resolution –very sensitive
160*120

## Slide 11: VM – blob detection
HSV
  H:[0,180], S:[0,255], V:[0,255]
  40<V<220, S>40
  Greatest blob is considered as sign
YCrCb
  Improvement of segmentation
  Greatest blob is considered as sign
HSV segmentation
YCrCb segmentation
Original
Notes: Donatas
Detection Segmentation method? - HSV vs YCrCb Thresholding
Thresholding by hsv,
Cr - red-difference chroma components

## Slide 12: VM – Sign classification
Center of mass
Center of bounding rectangle
Increment of
distance d
Fill ratio
Check d (is arrow or not?)
If d<thr  check ‘Fill ratio’
Notes: Enric
How to identify different signs? We already have blobs and boundedbox Explain two steps

## Slide 13: VM - Angle detection
Angle from moments
Angle from fitting line
Use of moments and center of bounding box
Poor precision, not smooth
Use of ‘line fitting’  Better precision on angle
Moments and center of bounding box  direction
Notes: Enric
How line fitting improves the smoothness of the results and the precision.
Still use of center of mass and center of bounding box for getting the direction where the line points.

## Slide 14: VM – Division area
PERCEPTIVE AREA
- Performs detection of sign
- Align the robot to the sign
PROXIMITY AREA
- Gets info (sign, angle, etc.)
- Execute according sign
FOV
Notes: Enric

## Slide 15: VM – Addition of IR LED
  Improvement only in low light condition
  Cheap and easy to implement
IR LED board
IR LED testing
Notes: Enric

## Slide 16: VM - Field of View
Before
After
~90cm
~50 cm
Position comparison
Notes: Donatas
Since we already had assembled hardware, we couldn’t change too much….
Again , for compensating perspective view

## Slide 17: State Manager
  WIGGLING
  Constant angular
  Zero linear speed
  Detecting signs
State manager diagram
Notes: Igor

## Slide 18: State Machine
  APPROACHING SIGN
  Constant linear
  Variable angular
  Aligning the object to the center of the FOV
State manager diagram
Notes: Igor

## Slide 19: State Machine
  EXECUTING COMMAND
  Game Over: Circle
  5 sec. pause: Cross
  Error: rotation
  Aligning with the angle of arrow
State manager diagram
Notes: Igor

## Slide 20: State Machine
  IDLE
  Zero angular speed
  Zero linear speed
  Waiting for the object to go out the FOV
State manager diagram
Notes: Igor

## Slide 21: State Machine
  MARCHING FORWARD
  Constant linear speed
  Zero angular speed
  Detecting object
State manager diagram
Notes: Igor

## Slide 22: Motion module I
Motors
Encoders
Left
Right
Heading
Drive
Stop
Turn
Notes: Donatas
I2C bus system mode.
Motion module structure – two groups
controlling functions

## Slide 23: Motion module II
Robot wheel positioning
Notes: Donatas
Track distance
Wheel diameter
Possible error – very smal, since there are 360 encoder counts per one Wheel

## Slide 24: I/O Module
  Ultrasonic sensor measures distance of obstacles in front of robot.
  LCD provides visual feeddback of the current state.
  Speaker provides audio feedback, enhancing game experience
Notes: Andrey
I/O output module provides the interaction of the robot with static and dynamic environment.
The ultrasonic sensor helps the robot to avoid frontal obstacles.
The current state and action are displayed on the LCD screen.
Audio feedback is delivered via an external speaker.

## Slide 25: Limitations and issues
Resolution | RB Pi + PiCam FPS | RB Pi + Logitech C270 FPS
160x120 | 20 | 9
320x240 | 6.5 | 4.8
640x480 | 2.5 | 2.3
1280x720 | 0.6 | 0.6
  Low computational power of Raspbery Pi
  Team development on single device
  Low reliability of the WiFi connection
  No software available for GPU Access
  Cross-compatibility
  Balance between robustness and real-time
Resolution and image frequency relation
Notes: Andrey
Raspberry Pi has a very limited in performance hardware. In addition to being limited, the
hardware is also platform-specific. For example, a part of 512 Mb of RAM is required to be allocated for
the video memory.
It was challenging to synchronize the development of several people on a single device without stable
internet access.
In some cases, the stability of the hardware was not reliable for the operation. WiFi pen drive didn't
maintain stable connection as well as cause device reboot occasionally.
Even having built-in SoC GPU module, the software for performing parallel computations was not available.
Platform specificity was another issue. The code working on Windows or Ubuntu is not guaranteed to
compile on the Raspberry-Pi targeted Debian system.
Balance betwee robustness and real time -> consequence from the limited hardware performance.

## Slide 26: Press the button!
Start/Stop button
Notes: Andrey
Da best invention in the world.
The simplification of the user interaction with the device - one button to start and stop the program.

## Slide 27: Neural Network
  Improve robustness
  Training is slow, require a lot of data
  Training is run on powerful PC
  Classifier can run on Raspbery Pi for single image
  Scanning every frame for finding exact position is too expensive!
Notes: Igor

## Slide 28: Further improvements
  Diverse set of signs
  More complex game rules
  Higher performance hardware
  Dynamic gameplay
  Robustness for the classification
Notes: Andrey
Modification of the game towards complexity.
Hardware improvements -> GPU computation, More Distance sensors, built-in speaker, touch screen etc.
Software improvements -> Classification performance with respect to the hardware improvements.

## Slide 29: Conclusions
  Raspberry Pi fulfill all requirements with a satisfactory level of robustness.
  Team made of people with diverse set of skills is a must!
  Simple requirements, hidden complexity.
  Keep it simple, no overthinking.
  Develop modular solutions, they are easily adapted.
Notes: Andrey
Figuring out right things to do.

## Slide 30
Thank you for your attention!